## Slide 1: Introduction of Real-World Signals and Systems into ECpE DSP Laboratory Curriculum
Members:
Brady A. Max K.
Sam B. Emily L.
Mitchell H. Isaac R.
Advisor: Matthew Post
Client: Matthew Post Website: http://sddec20-14.sd.ece.iastate.edu/
Notes: Ren

## Slide 2: Problem Statement
Conceptualizing the signals and systems curriculum at Iowa State University can be frustrating for new students.
The CyDAQ team seeks to redesign the signal processing laboratory curriculum using the CyDAQ teaching platform to help alleviate this frustration.

## Slide 3: Introduction to CyDAQ
CyDAQ is a hardware teaching platform designed for EE 224/324 that contains onboard analog filters and interfaces for sampling data to a PC.
Our goal is to design labs and supplemental hardware that connect core concepts to real world hardware.
Figure 1: CyDAQ Board
Notes: Brady

## Slide 4: Conceptual Sketch
CyDAQ
Software/Firmware
Hardware
Labs
Embedded
Graphical Interface
FPGA
Signal Routing
Sampling
Band-limiting
Real-World Application
EE 224 & 324
Learning Objectives
Notes: Ren

## Slide 5: Hardware Requirements
Functional:
Variable sample rate
Adjustable analog filters
Low noise power delivery
Standard sensor interfaces
Digital to analog converter
Parallel signal handling
Non-Functional:
CyDAQ unit costs ~$350
Durability
  Physical
  Electrical
Expandable for future use
Well documented example of good hardware design
Notes: SAM

## Slide 6: Software Requirements
Functional:
Configure all analog filters
Concurrent sampling and sample storage
Simple GUI for lab use
  Constrained front-end for students
  Full-featured back-end for debugging
Non-Functional:
Responsive interface
Impervious to serial data loss
90% code coverage for unit tests
Well documented; example of good software design
Notes: Brady

## Slide 7: Lab Requirements
Functional:
Follow class learning objectives
Use real-world application as lab motivation
Create 4+ labs for EE 224 and EE 324
Non-Functional:
Doable by 1-2 students in 2-4 hours
Made in LaTeX; visually pleasing
Serves as an example for additional ECpE course labs
Notes: Ren

## Slide 8: Additional Constraints & Considerations
COVID-19 Impact
  Reduced number of labs created and put into EE 224 Spring 2020 semester
  Reduced amount of feedback from students in lab
  Modified lab documents to fit online classes
Economic Considerations
  Cost to produce, repair, and replace
  Environmental impact and power efficiency
Notes: Max

## Slide 9: WhyDAQ?
Market Alternatives
  National Instruments MyDAQ
    Similar feature set, but lacks programmability and expandability
    Tied to NI’s suite of software
    $371.00
  National Instruments Elvis III
    Improved expandability, includes FPGA
    Tied to NI’s suite of software
    $2,897.00
Figure 2: NI MyDAQ
Figure 3: NI Elvis III

## Slide 10: WhyDAQ?
University-developed platform
  Designed with the ECpE DSP curriculum in mind
  Open source software, written in industry standard Python and MATLAB
  Expandable to fill teaching needs of many classes in both lecture and lab
  Fully programmable Xilinx FPGA
  Compatible with industry standard lab tools, designed for Digilent Analog Discovery multi-function instrument
  Total BOM cost of ~$500
    Includes Digilent Analog Discovery
Figure 4: Xilinx Zybo Z7
Figure 5: Digilent Analog Discovery 2
Notes: max

## Slide 11: Potential Risks & Mitigation
Risk: Components of the CyDAQ are damaged due to student abuse Mitigation: CyDAQ and FPGA are enclosed in a transparent polycarbonate box
Risk: FPGA is damaged by the addition of incorrectly added hardware components Mitigation: Team members read datasheets and become knowledgeable about components and pinouts before connecting to the FPGA
Risk: Hardware component delays due to COVID-19 Mitigation: Team members order components early and expect delays in shipping
Notes: Ren

## Slide 12: BOM Cost
Part | Cost
PCB Components | $112.29
Enclosure | $22.60
Mounting Hardware | $16.39
Zybo Z7 | $199.00
Digilent Analog Discovery 2 (DAD) | $279.00
Total (without DAD) | $350.28
Total (with DAD) | $629.28

## Slide 13: Project Schedule
Notes: max

## Slide 14: CyDAQ Fundamentals
GUI
CyDAQ
Zybo
PC
1st Order High Pass
1st Order Low Pass
2nd Order Band Pass
6th Order High Pass
6th Order Low Pass
6th Order Band Pass
Sample Output
Signal Input
Python
MATLAB
Analog Sensor
Notes: Mitchell

## Slide 15: CyDAQ Fundamentals - CyDAQ Hardware
Analog Signal Flow Control
  Input select configurable through I2C controlled multiplexers.
  Input level shifting and impedance isolation
  Output filtering and impedance isolation
Analog Filter Configuration
  Signal band-limiting configurable through I2C controlled solid-state potentiometers
  Filter order stacking and corner selection programmable from FPGA platform
Digital Signal Processing
  Analog to digital Conversion through FPGA XADC input driver / level shifter
  Digital to analog Conversion through SPI fed external DAC integrated circuit
Notes: SAM

## Slide 16: CyDAQ Fundamentals - Zybo Firmware
Single-Core ARM Application
  Handles scheduling logic, sampling, and PC software interface
  FreeRTOS operating system to allow parallel operations
FPGA Programmable Logic cores
  XADC core performs 1MS/s sampling
  AXI GPIO cores allow general sensor interfaces
  Other custom-made cores added as necessary for labs
    Flexible firmware is a key feature of CyDAQ
Notes: Brady

## Slide 17: CyDAQ Fundamentals - PC Software
MATLAB Front-end
  Handles user interactions through buttons, text boxes, and selectors to configure and sample the board.
  Sampled data can be exported to .csv or .mat file
Python Back-end
  Verification of the given parameters
  Communication to the Zybo FPGA over USB.
Figure 6: GUI Start Page
Notes: Mitchell

## Slide 18: Technology Platforms
Hardware
  Low-noise Switch Mode Power Supplies (SMPS PMICs)
  I2C configurable solid state potentiometers
  I2C configurable signal routing multiplexers
  Zybo FPGA development board direct mount
  UART Serial PC connectivity
  SPI Digital to Analog Conversion capability expansion
Software
  Python
  MATLAB App Designer
  JSON
Notes: SAM
JSON - for saving/ loading Zybo configurations from the user-side
Python - communication from the PC to the Zybo
MATLAB - GUI design and data manipulation

## Slide 19: Test Plan
Software
  Unit Testing
    Testing each function such that no input yields an unexpected output or error
    Code coverage goal should be ~90%
  UI Testing
    Testing the interaction of the UI components leads to the correct state of the program
    Most commonly used UI components should be tested
    Chances of catching an error is low, but highly valuable if one is found.
  Integration Testing
    Build tests such that interaction between components is sound during test runs, but also runtime tests occur incase connection is broken or cannot be established and contingencies must be dispensed.
Notes: Mitchell

## Slide 20: Current Implementation
CyDAQ Designed by ETG
  Single-process high-level firmware
  Minimal GUI
  Fully-featured filter board
  Variety of interfacing options for peripheral hardware
  Supply of base CyDAQ units fabricated and ready for deployment
  No peripheral modules designed
  No labs designed around the CyDAQ
Figure 7: CyDAQ in Polycarbonate Case
Notes: Max

## Slide 21: Project Status (with respect to milestones)
Hardware
DAC evaluation module completed and ready for characterization
Parallel XADC passive input level shifter completed, tested, validated
Software
The GUI is being laid out with integration with Python happening concurrently
Labs:
Completion of ¾ labs for 224 and began conceptualizing lab documents for EE 324
Tested one lab with EE 224 students with feedback to be received after semester completion
Notes: Brady

## Slide 22: Member Responsibilities
Brady A.
  Embedded Systems - Firmware development and testing
Sam B.
  Hardware Expansion Design
  Hardware Design Requirements
  Lab Development
Mitchell H.
  Web Designer
  GUI Designer
Max K.
  Lab Development
    Noise Reduction Lab
  Soldering and hardware assembly
Emily L.
  Lab Development including:
    Noise Reduction Lab
    Final Project Labs
Isaac R.
  Team Communication Lead
  Hardware Design And Implementation
  Lab Development
Notes: Mitchell
BA - programming the firmware and embedded systems on the Zybo
Sam - Hardware lead, responsible for designing the CyDAQ board
Max - Hardware assistant and lab drafter
Emily - Lead lab drafter
Isaac -

## Slide 23: Project Timeline
Spring 2019
Requirements Defined, Analog Filters Redesigned
Functional design and validation of filters
State variable filter
Digital control scheme
Fall 2019
Platform Hardware Redesign
Design and validation of power delivery
Sensor interfaces
Full I/O definition
Mechanical definition
Spring 2020
Lab Design,
Software Development
Curriculum integration
User interface design
Platform firmware
Control flow development
Expanded functional requirements
Fall 2020
Hardware Expansion,
Lab Implementation
Final hardware revision
PMOD expansion development
Lab document delivery
Notes: SAM

## Slide 24
Thank you for listening!