## Slide 1: Introduction of Real-World Signals and Systems into ECpE DSP Laboratory Curriculum
Members:
Brady A. Max K.
Sam B. Emily L.
Mitchell H. Isaac R.
Team: SDDEC20-14
Advisor: Matthew Post
Client: Matthew Post Website: http://sddec20-14.sd.ece.iastate.edu/
Contact: Isaac Rex (irex@iastate.edu)
Notes: Ren

## Slide 2: CyDAQ Recap
CyDAQ is a hardware teaching platform designed for EE 224/324 that contains onboard analog filters and interfaces for sampling data to a PC.
Our goal is to design labs and supplemental hardware that connect core concepts to real world hardware.
Figure 1: CyDAQ Board
Notes: Max

## Slide 3: Conceptual Sketch
CyDAQ
Software/Firmware
Hardware
Labs
Embedded
Graphical Interface
FPGA
Signal Routing
Sampling
Band-limiting
EE 224 & 324
Learning Objectives
Real-World Application
Notes: Max

## Slide 4: Goals
Create and submit lab documents for EE 324 and EE 224
  EE 224 Labs & Final Project
    3 completed, 1 nearing completion
  4+ Labs for EE 324
    1 completed, 1 nearing completion, 3 outlined
Final CyDAQ device revision
  Expand sampling bandwidth with SPI differential ADC
    Test implementation on eval board, anti-aliasing filter designed
  Add SPI DAC to broaden application potential
    Hardware added to eval board, firmware development in progress
  Revise FPGA firmware to utilize FreeRTOS parallel processing
    FreeRTOS doesn’t fit our use case; had success with an interrupt-based design
Notes: Brady

## Slide 5: Technical Challenges
Hardware:
Completed Filter Design for ADC
Tested DAC and ADC evaluation module
Validated data conversion designs
Added DAC and ADC designs to main PCB and updated PMIC layout

## Slide 6: Technical Challenges & Progress: Anti - Aliasing Filter for ADC
Design:
2nd order multiple-feedback filter with 1st order LC low-pass
Fully differential, DC coupled to ADC
Shares common mode reference with analog measurement reference

## Slide 7: Technical Challenges & Progress: ADC and DAC Validation
Design:
Tested SPI communication
Sampled ADC input
Observed DAC output
Validated data bus design and protocol for both devices

## Slide 8: Technical Challenges & Progress: PCB Layout Revision
Layout Changes:
Condensed PMIC block
Integrated DAC input
Integrated ADC output

## Slide 9: Technical Challenges & Progress: Software Systems
Firmware:
FreeRTOS determined insufficient
  Task scheduler runs at 1kHz
  Offers no benefits for a 1MHz+ sampling application
Interrupt-based firmware at feature parity
  ISRs to process ADC and DAC operations
  Passive loop to poll UART in background
SPI controller
  Drive DAC and read external ADC
  Added to FPGA fabric, configuration in progress
Notes: Brady

## Slide 10: Technical Challenges & Progress: User Interface
Connecting Python to MATLAB
Automatic Updates for Patches
Fetching instead of Streaming
Notes: Mitch

## Slide 11: Technical Challenges & Progress
Labs:
Introduction to Noise Filtering
  Filtering a noisy sound file
  Identifying and implementing the correct filter using the CyDAQ
Heart Rate Project Lab
  Open-ended design lab
  Pulse Sensor input
  Heart rate graph, BPM output
Completed: Image Restoration Lab
In-progress: Power Systems Design Lab for EE 324
Notes: Ren

## Slide 12: Technical Challenges & Progress
Labs:
Control Systems I: Measuring Loop Response
  Parameter measurement
  Power supply design
  Control loop tuning
  Application Notes
Control Systems II: Controller Design
  System modeling and simulation
  Tool-based controller design
  Real implementation
Notes: Isaac

## Slide 13: Technical Challenges & Progress
Labs:
System Dynamics From Differential Equations
  Complete redesign of lab 1 for EE 324 to incorporate real world hardware
  Mechanical spring system utilizing CyDAQ to sample data
  Analysis of an RLC circuit, comparing theoretical and practical results
  Deriving differential equations for lab models
Notes: Max

## Slide 14
Thank you for listening!
Questions? Contact us at sddec20-14@iastate.edu
Summary:
Finalized hardware updates
Delivered beta software for GUI and firmware backend
Completed several labs connecting theory to application
Notes: Ren